|  | ExMC(Seoul/WG1+WG5)/07 Draft rev IECEx 02 October 2002 |
| --- | --- |

INTERNATIONAL ELECTROTECHNICAL COMMISSION

IEC SCHEME FOR CERTIFICATION TO STANDARDS FOR SAFETY OF 
ELECTRICAL EQUIPMENT FOR EXPLOSIVE ATMOSPHERES (IECEx SCHEME)

Ex Management Committee (ExMC)

Rules of Procedure of the IEC Scheme for Certification to Standards for Electrical Equipment for Explosive Atmospheres (IECEx Scheme), Publication IECEx 02.

- - - - - - - - - -

Introduction

This document has been prepared following the Combined meeting of WG1 and WG 5 held in Seoul 18+19 October 2002 and is submitted for consideration by ExMC Members during the Seoul 2002 meeting

This document incorporates changes to ExMC/129/CD, as proposed by the WG1/WG5 meeting.

Changes to ExMC/129/CD are highlighted

CONTENTS

1	Scope	9

2	Normative references	9

3	Definitions	10

4	Governing of the IECEx Scheme	12

5	Principles of the IECEx Scheme	13

5.1	Certificate of Conformity	13

5.2	Method of Application	13

5.3	Acceptance	13

5.4	Permissions	13

5.5	Exchange of Certificates	13

5.6	Objective	13

6	Confidentiality	14

7	Participating countries	14

7.1	Participation	14

7.2	National differences	14

7.3	Participating country	14

7.4	Changes	14

1.1	Termination	14

7.5	14

7.6	Withdrawal	14

8	IECEx instruments	15

8.1	IECEx Certificate of Conformity	15

8.1.1	Issue	15

8.1.2	Layout	15

8.1.3	Contents	15

8.2	IECEx Ex Test Report (ExTR)	15

8.2.1	Preparation	15

8.2.2	Description of equipment	15

8.2.3	Layout	15

8.2.4	Issue	16

8.2.5	Restrictions	16

8.2.6	Copies	16

8.3	IECEx Quality Assessment Report	16

8.3.1	Content	16

8.3.2	Layout	16

8.3.3	Issue	16

8.3.4	Restrictions	16

8.3.5	Copies	16

8.4	IECEx Mark of Conformity*	16

9	Certification procedure	17

9.1	Applicant	17

9.2	Documentation	17

9.3	Samples	17

9.4	Examination	17

9.5	Assessment of Quality Plans	17

9.6	Completion	17

9.7	Surveillance	18

9.8	Changes	18

9.9	Ensuring conformity	18

9.10	Documentation retained	18

9.11	Surcharges	18

9.12	Suspension or withdrawal	18

9.13	Notification of withdrawal	19

10	Use of ExTRs and QARs for National Certification	19

10.1	Documentation	19

10.2	National Certification	19

10.3	Compliance with rules	19

10.4	Invalid ExTR	20

10.5	Appeals	20

11	Acceptance of certification bodies and assessment and testing laboratories	20

11.1	Acceptance of certification bodies	20

11.1.1	Conditions for acceptance	20

11.1.2	Application	20

11.1.3	21

11.1.4	Assessment	21

11.1.5	Resolution of differences	21

11.1.6	Report to ExMC	21

11.1.7	Acceptance	21

11.1.8	Notification	22

11.1.9	Changes	22

11.1.10	Extension of scope	22

11.1.11	Reporting of decisions	22

11.1.12	Re-assessment	22

11.1.13	22

11.1.14	23

11.2	Acceptance of  Ex testing laboratories	23

11.2.1	23

11.2.2	23

11.2.3	23

11.2.4	24

11.2.5	24

11.2.6	24

11.2.7	24

11.2.8	24

11.2.9	24

11.2.10	25

11.2.11	25

11.2.12	25

11.2.13	ExTR Review	25

12	IECEx publications	25

12.1	Types of publications	25

12.2	Information to be available	25

12.3	IECEx Bulletin	26

12.4	IECEx Newsletter	26

12.5	Source of information	26

13	Complaints	26

Annex A Application from a candidate Member Body of the IECEx Scheme  to become a participating country in the IECEx Scheme	27

Annex B Declaration by a certification body applying to become an Ex Certification Body	28

Annex C Declaration by an assessment and testing laboratory applying for acceptance as an IECEx  Ex Testing Laboratory	29

Annex D Information to be provided by an assessment and testing laboratory in applying for acceptance	30

D.1	30

D.2	30

D.3	Senior management	30

D.3.1	30

D.3.2	30

D.3.3	30

D.3.4	30

D.4	Employees	30

D.4.1	30

D.4.2	31

D.4.3	31

D.5	Equipment	31

D.6	Test facilities and services	31

D.6.1	31

D.6.2	31

D.6.3	31

D.7	Other information	31

D.7.1	31

D.7.2	31

D.8	Quality Management Policy	32

D.8.1	32

D.8.2	32

D.8.3	32

D.8.4	32

D.9	Work instructions	32

D.9.1	32

D.9.2	32

D.9.3	32

D.9.4	32

D.9.5	32

D.10	Personnel	32

D.10.1	32

D.10.2	32

D.11	Test equipment and calibration	33

D.11.1	33

D.11.2	33

D.11.3	33

D.11.4	33

D.11.5	33

D.12	Test procedures	33

D.12.1	33

D.12.2	33

D.12.3	33

D.12.4	33

D.12.5	33

D.13	Handling and storage	34

D.13.1	34

D.13.2	34

D.13.3	34

D.13.4	34

D.13.5	34

D.13.6	34

D.14	Records	34

D.14.1	34

D.14.2	34

D.14.3	34

D.15	Test reports	34

D.15.1	34

D.15.2	35

D.16	Preparedness for assessment	35

D.16.1	35

D.16.2	35

D.16.3	35

INTERNATIONAL ELECTROTECHNICAL COMMISSION

Rules of Procedure of the Scheme of the IEC
for Certification to Standards for Electrical Equipment
for Explosive Atmospheres (IECEx Scheme)

FOREWORD

This publication has been prepared by the Ex Management Committee.

All of the annexes to this publication are normative.

This publication is directly related to Publication IECEx 01 containing the Basic Rules of the IECEx Scheme.

INTRODUCTION

To be completed

Overview of IEC Ex Scheme

Rules of Procedure of the Scheme of the IEC
for Certification to Standards for Electrical Equipment
for Explosive Atmospheres (IECEx Scheme)

Publication IECEx 02

# Scope

This publication contains the Rules of Procedure of the Scheme of the IEC, hereinafter referred to as the "Rules", for the certification of electrical equipment which is intended for use in explosive atmospheres and which complies with one or more of the IEC standards defining the types of protection against causing an explosion  (IECEx Scheme).

The IECEx Scheme becomes operative for each type or concept of protection as soon as at least three certification bodies from different countries have been accepted for that type or concept of protection.

A list of current standards in use is published in the IECEx Bulletin (see 12.3) and on the IECEx Website (www.iecex.com).

These Rules relate to the Basic Rules of the IECEx Scheme, as given in Publication IECEx 01.

NOTE - The IECEx Scheme is applicable to equipment and services e.g. Repair and Overhaul, conforming to standards prepared by IEC TC31 and its subcommittees, which currently include the following:

-	flameproof enclosures (IEC 60079-1)

-	type of protection ‘p’ (IEC 60079-2)

-	sand-filled apparatus (IEC 60079-5)

-	oil-immersed apparatus ‘o’ (IEC 60079-6)

-	increased safety ‘e’ (IEC 60079-7)

-	intrinsic safety  ‘i’ (IEC 60079-11)

-	electrical apparatus with type of protection ‘n’ (IEC 60079-15)

-	encapsulation ‘m’ (IEC 60079-18)

-	repair and overhaul (IEC 60079-19)

-	dust proof and dust protected enclosures (IEC 61241-1)

-	others, e.g. Trace heating and caplights

# Normative references

The following publications contain provisions which, through reference in this text, constitute provisions of these Rules. At the time of publication, the editions indicated were valid. The Ex Management Committee shall decide the timetable for the introduction of revised editions of the publications.

IECEx 01: 1999, Basic Rules of the IECEx Scheme.

ISO/IEC Guide 2: 1996, Standardization and related activities - General vocabulary.

ISO/IEC 17025: 1990, General requirements for the competence of calibration and assessment and testing laboratories.

ISO/IEC Guide 65: 1996, General requirements for bodies operating product certification systems.

# Definitions

ISO/IEC Guide 2 gives the basic definitions.

For the purpose of the IECEx Scheme, the following definitions apply:

3.1

IECEx Scheme

Scheme of the IEC for the certification of electrical equipment intended for use in explosive atmospheres and applicable to equipment embodying one or more of the types of protection covered by IEC standards prepared by IEC Technical Committee No. 31

3.2

type or concept of protection

the specific measures applied to electrical equipment to avoid ignition of a surrounding explosive gas atmosphere.

[IEC 60079-0: 2000]

3.3

Ex apparatus

items applied as a whole or in part for the utilization of electrical energy and incorporating one or more types of protection for potentially explosive atmospheres.   These include, among others, items for the generation, transmission, distribution, storage, measurement, regulation, conversion and consumption of electrical energy and items for telecommunications.

3.4

Ex component

a part of electrical apparatus or a module (other than an Ex cable entry), marked with the symbol "U", which is not intended to be used alone and requires additional certification when incorporated into electrical apparatus or systems for use in potentially explosive atmospheres.

3.5

Ex system

an assembly of interconnected items of Ex apparatus for which the interconnection has to be carried out in accordance with the descriptive system document in order to comply with the explosion protection requirements.

3.6

Ex equipment

a general term applying to Ex apparatus, Ex components and Ex systems.

3.7

IECEx Certificate of Conformity

document issued under these Rules indicating that adequate confidence is provided that a duly identified product is in conformity with a specific standard.   The certificate can relate to Ex apparatus, an Ex component or an Ex system.

(ISO/IEC Guide 2: 1996, term 15.5 modified(

3.8

IECEx Mark of Conformity*

-----------

*  under development

3.9

IECEx Ex Test Report (ExTR)

a document issued by an ExTL that includes an evaluation record, product design assessments and other relevant information assessed and endorsed by the issuing ExCB demonstrating that the examined product type is in conformity with specified standards.

3.10

Evaluation record

A document that is prepared, signed and issued by an ExTL which presents product test results.   It shall give, as far as necessary, for each clause of the relevant standard a brief reference to the requirements, and the results of tests and examinations.   It shall also contain the information necessary for identification of the Ex equipment such as type designation, ratings, description and photographs.

3.11

Ex Management Committee (ExMC)

the body which administers the operation of the IECEx Scheme and is responsible to the Conformity Assessment Board of the IEC.

3.12

Ex Testing and Assessment Group (ExTAG)

the body which deals with questions of practice relating to assessment and testing under the IECEx Scheme and is responsible to the Ex Management Committee.

3.13

Member Body of the IECEx Scheme

a body which has been accepted according to the Basic Rules of the IECEx Scheme, Publication IECEx 01 and to these Rules of Procedure, and which is either a National Committee of the IEC or a body notified to the ExMC by the National Committee of the IEC.

3.14

Ex Certification Body (ExCB)

a body which has been accepted according to these Rules and which issues IECEx Certificates of Conformity and IECEx Ex Test Reports.

3.15

IECEx Assessment and Testing Laboratory (ExTL)

an assessment and testing laboratory which is accepted according to these Rules and which is either integral with, or under the complete control of, or belongs to or works under a written agreement for an Ex Certification Body.

3.16

national differences

those requirements or test parameters in the corresponding national standard which, when applied to equipment complying only with the standard accepted for use in the IECEx Scheme, might entail non-compliance of that equipment with the relevant national standard.

NOTES

1   When a requirement in the IEC standard is not implemented in the corresponding national standard, that is also a national difference.

2   Those restrictive requirements in a national standard, which do not deviate from the criteria included in the corresponding standard accepted for use in the IECEx Scheme, but which limit the possibility to offer the relevant equipment for sale in the country concerned, are also considered to be national differences.

3.17

applicant

a firm or a person who applies to an Ex Certification Body for obtaining an IECEx Certificate of Conformity or an IECEx Ex Test Report.

3.18

manufacturer

an organization, situated at a stated location or stated locations, that carries out or controls such stages in the manufacture, assessment, handling and storage of a product that enables it to accept responsibility for continued compliance of the product with the relevant requirements and undertakes all obligations in that connection.

3.19

IECEx Bulletin

bulletin, issued at intervals decided by the Ex Management Committee, containing detailed technical and procedural information about the IECEx Scheme.

3.20

IECEx Register

register, issued at intervals decided by the Ex Management Committee, containing information on all Accepted Certification Bodies and IECEx Assessment and Testing Laboratories and listing all IECEx Certificates of Conformity.

3.21

IECEx Newsletter

newsletter, issued at intervals decided by the Secretary of the Ex Management Committee, to promote the IECEx Scheme amongst users and prospective users of the Scheme and to inform users of significant developments of the Scheme.

3.22

IECEx Quality Assessment Report (QAR)

a document that presents the results of an on-site assessment of a manufacturer’s quality control system, by an ExCB, to the requirements of the IECEx Scheme

# Governing of the IECEx Scheme

The IECEx Scheme shall be governed by the Ex Management Committee (ExMC), whose responsibilities in this respect are defined in the Basic Rules of the IECEx Scheme, Publication IECEx 01.

This document, (IECEx 02) sets out the general rules and procedures of the IECEx Scheme.  These general rules are supplemented by the Scheme’s Operational Documents.   These Operational Documents are available to all IECEx Member Bodies, ExCBs and ExTLs, including candidate ExCBs and ExTLs and to manufacturers that have applied for either an IECEx Certificate of Conformity, IECEx ExTR or IECEx QAR.

# Principles of the IECEx Scheme

## Certificate of Conformity

The IECEx Scheme provides the means for manufacturers of Ex equipment to obtain certificates of conformity that will be accepted in all participating countries as equivalent to their national certification.   A certificate of conformity may be obtained from any certification body accepted into the Scheme. The certificate will attest that the equipment design conforms to the relevant IEC standards and that the manufacturer is manufacturing the product under a quality plan meeting the requirements of this Scheme and under the surveillance of an ExCB. Manufacturers holding certificates of conformity may affix the IECEx Mark of Conformity* to equipment that they have verified as complying with the certified design.

## Method of Application

An application for a country to participate in the IECEx Scheme is made on a standard by standard basis by the candidate Member Body of the IECEx Scheme for that country.   The application is made to the Secretary of the ExMC.   Certification  bodies and assessment and testing laboratories wishing to be accepted into the Scheme must reside in an IECEx participating country.   Their application to be accepted is made through the Member Body of the IECEx Scheme for the country in which they reside.

## Acceptance

Certification bodies and assessment and testing laboratories are accepted into the IECEx Scheme following satisfactory assessment of their competence by assessors selected by the ExMC as providing adequate confidence to regulatory authority, user, manufacturer and certification body interests. Competence is judged by reference to ISO/IEC 17025 and Guide 65 and IECEx Technical Guidance Documents.

## Permissions

ExCBs that reside in an IEC participating country are permitted to issue IECEx ExTRs, QARs and IECEx Certificates of Conformity.

## Exchange of Certificates

ExCBs located in countries that do not accept IECEx Certificates of Conformity or whose national standards are not yet identical to the IEC standards, shall accept for review IECEx ExTRs and QARs for the purposes of issuing local national certification, thereby providing a “fast track” to national certification.

IECEx ExTRs may cover national differences of the accepting country.   An ExCB receiving an ExTR or QAR may review the documentation for completeness.   Should the ExCB receiving an ExTR or QAR believe it to contain errors, shall contact the issuing ExCB before taking any action.

## Objective

The final objective of the IECEx Scheme is world wide acceptance of one standard, one certificate and one mark.

# Confidentiality

All those participating in the IECEx Scheme shall respect the confidentiality of any information that they obtain and take all reasonable steps to bind their staff and those working under contract to preserve that confidentiality.

# Participating countries

## Participation

In order for a country to participate in the IECEx Scheme, the candidate Member Body of the IECEx Scheme shall make an application to the Secretary of the ExMC in the form of Annex A.

## National differences

The Member Body of the IECEx Scheme and the ExMC shall specify national differences from the IEC standard(s) in the application.

## Participating country

Once the application has been approved by the ExMC, the country shall be deemed to be a participating country.

## Changes

The Member Body of the IECEx Scheme shall notify the ExMC of any changes in the national differences declared in its application.

## Termination

The ExMC may terminate a country's participation in the IECEx Scheme if the country persists in a breach of these Rules after due warning by the ExMC to the Member Body of the IECEx Scheme.

## Withdrawal

In the event of a country’s ceasing to be a participating country, the ExCBs in that country shall lose the right to issue new IECEx Certificates of Conformity and ExTRs.   IECEx Certificates of Conformity shall remain valid for a period of 6 months following which they shall be withdrawn.

ExTRs previously issued shall remain valid. QARs shall remain valid for a period of 6 months. Within this period the manufacturer shall seek an alternative ExCB that accepts to maintain the validity of the QARs

# IECEx instruments

## IECEx Certificate of Conformity

### Issue

An IECEx Certificate of Conformity is issued by an ExCB, on the basis of an ExTR and QAR, certifying that the type of Ex equipment identified on the Certificate conforms in all relevant respects with the IEC standard(s) specified on the Certificate and that the manufacturer named on the Certificate manufactures the product under quality plans complying with the requirements of this Scheme, as a means of providing adequate confidence that the Ex equipment will be produced in conformity with the design of the certified equipment.

### Layout

The ExMC shall decide on the layout and content of IECEx Certificates of Conformity

### Contents

The IECEx Certificate of Conformity shall contain at least the following information:

clear description of the Ex equipment,

the name and address of the manufacturer

the IEC Standard, edition and amendments, if any

reference to the supporting ExTR

Ex marking requirements

Name of the issuing ExCB

Conditions of safe use, if any

List of certification drawings used to obtain the certification

## IECEx Ex Test Report (ExTR)

### Preparation

An ExTR is prepared by an ExTL and endorsed and issued by an ExCB recording the product design assessment, examination and assessment and testing work carried out in order to verify the conformity of Ex equipment with the requirements of the stated standards.

### Description of equipment

The ExTR shall contain a clear description of the Ex equipment, the name and address of the applicant and the manufacturer and the edition of the IEC standard, and amendments, if any. It shall give, as far as necessary, for each clause of the relevant standard a brief reference to the requirements, and the results of tests and examinations. The ExTR shall also contain the information necessary for identification of the Ex equipment such as type designation, ratings, description and photographs.

### Layout

The ExMC shall decide on the layout and content of ExTRs.

### Issue

ExTRs are issued along with an IECEx QAR and IECEx CoC.   The ExTR may include evaluation of the Ex equipment for conformity with declared national differences, and may be used by other ExCBs in the national certification of the equipment.

### Restrictions

Because ExTRs are transitory documents used in the preparation of IECEx Certificates of Conformity, they shall not be used in any form of advertising or sales promotion in order that the information is not misrepresented.

### Copies

When a copy of an ExTR is required, it shall be reproduced in its entirety.

## IECEx Quality Assessment Report

### Content

A QAR is prepared and issued by an ExCB recording the assessment of a manufacturer’s quality control system used to ensure the on-going compliance of Ex products with those characteristics that are covered by the ExTR.  The assessment includes assessing conformity of the manufacturer’s quality control system with the requirements of the IECEx Scheme in addition to assessing the implementation of the quality controls by the manufacturer. . A QAR has a limited duration (3 years) and can be withdrawn or suspended if intermediate follow-up assessments are not satisfactory. ExCB shall pass a copy of the QARs to the ExMC Secretary who shall maintain a central registry and list of QARs. The ExMC secretary shall be informed without delay of any suspension or withdrawal of QARs.

### Layout

The ExMC shall prepare a document detailing quality requirements for the Scheme and the layout and content of QARs.

### Issue

The QAR may be issued by ExCBs for the purpose of acceptance by other ExCBs in the national certification of the equipment.  The QAR shall refer to a specific manufacturing site.

### Restrictions

Because QARs are transitory documents used in the preparation of IECEx Certificates of Conformity, they shall not be used in any form of advertising or sales promotion in order that the information is not misrepresented

### Copies

When a copy of an QAR is required, it shall be reproduced in its entirety

## IECEx Mark of Conformity*

# Certification procedure

## Applicant

An application for an IECEx Certificate of Conformity may be made by an applicant to any ExCB for the relevant standard(s).   The applicant may be a manufacturer or may act on behalf of a manufacturer. In the latter case, evidence shall be submitted that the applicant is authorized to act on behalf of the manufacturer for the application and that the manufacturer undertakes to abide by the Rules and obligations of the IECEx Scheme.   The Certificate shall be issued in the name of the manufacturer.

## Documentation

The documentation submitted by the applicant shall accurately identify the Ex equipment for which certification is required, the standard(s) to which certification is to be granted, and the manufacturer responsible for the conformity of production items with the design of the certified equipment.

## Samples

The applicant shall supply the documentation necessary to specify the explosion protection features of the Ex equipment.   The applicant shall supply such samples of the Ex equipment as the ExCB deems necessary.

## Examination

The ExCB shall arrange for an ExTL to examine the documentation and the sample(s) to verify that the Ex equipment design is in conformity with the standard(s).   The ExTL shall examine the sample(s) for compliance with the documentation, test the sample(s) as specified in the standard(s) and compile an ExTR.

## Assessment of Quality Plans

The ExCB shall assess the conformity of the manufacturer's quality plan(s), associated with the quality system, with the requirements of the IECEx Scheme.  Refer to IECEx XXXXX . In order to demonstrate how the quality system ensures that equipment is manufactured in conformity with the design of the certified equipment, the manufacturer shall provide the ExCB with a copy of a quality plan for the equipment.   The manufacturer may provide evidence of the suitability of the quality system such as certification/registration to ISO 9001 by a competent body.  The ExCB shall take the evidence into account when deciding the extent of the assessment which it needs to conduct.   The ExCB shall issue an IECEx QAR.

## Completion

Upon satisfactory completion of the work, the ExCB shall endorse the ExTR and QAR which together with an IECEx Certificate of Conformity shall be issued to the applicant, with a copy of each being retained by the ExCB.   The manufacturer and the ExCB shall each retain a set of the documentation referred to in the certificate.   The ExCB shall send a copy of the Certificate to the Secretary of the ExMC along with details of the ExTR and QAR.

## Surveillance

The ExCB shall carry out, or arrange for another body to carry out on its behalf, periodic surveillance of the manufacturer's quality system and quality plan(s) as well as periodic examination and, if indicated to be necessary, assessment and testing of representative samples of certified Ex equipment.   The frequency of such surveillance, inspection and assessment and testing shall be determined by the ExCB in the light of the effectiveness of the manufacturer's quality plan(s).   Such frequency shall take into account whether the manufacturer holds current ISO 9001 certification/registration by a competent body.

## Changes

If the manufacturer wishes to make a change to the certified Ex equipment, he shall apply to the ExCB which granted the IECEx Certificate of Conformity, describing the change and the measures adopted to ensure continuing conformity with the relevant standard(s).   The ExCB shall arrange for such work as is necessary to be carried out to verify that the Ex equipment incorporating the change will still conform to the standard(s).   The ExCB shall issue an addendum to the Certificate authorizing the change. The layout and content of the addendum shall be specified by the ExMC. The ExMC shall determine the extent of the change which can be accommodated using an addendum to the original Certificate.   Major changes could require a new Certificate to be issued.

## Ensuring conformity

The manufacturer has the responsibility to ensure that all Ex equipment to which the IECEx Mark of Conformity* is affixed and all Ex equipment that is described as "IECEx certified" is in conformity with the design of the certified equipment.   Failure to do so, and any other misuse of the Mark, could lead to suspension or withdrawal of the IECEx Certificate of Conformity by the ExCB.

## Documentation retained

The ExCB has the right to keep for future reference photographs, technical documentation and, by agreement with the applicant, samples or, for large equipment, parts of such equipment. Such reference material shall be confidential.

## Surcharges

An applicant who is not in a participating country and an applicant acting on behalf of a manufacturer in such a country shall pay a contribution to the costs of the IECEx Scheme in the form of a surcharge for each application.

## Suspension or withdrawal

An IECEx Certificate of Conformity may be suspended or withdrawn by the issuing ExCB if

it has been issued in error,

the holder requests cancellation,

it is used in a misleading way,

the Ex equipment no longer corresponds to the design of the certified equipment, or

the manufacturer's quality system and associated quality plan no longer provides adequate confidence that Ex equipment will be produced in conformity with the design of the certified equipment.

The ExCB shall give due notice to the manufacturer of such suspension or withdrawal and shall give the reason(s).

While a Certificate is suspended or when it has been withdrawn, the manufacturer shall no longer describe the Ex equipment as "IECEx certified", nor shall he affix the IECEx Mark of Conformity* to the Ex equipment.   Equipment already supplied prior to the withdrawal of the Certificate is not affected.

## Notification of withdrawal

When an IECEx Certificate of Conformity has been withdrawn, the Secretary of the ExMC shall be notified as soon as possible by the issuing ExCB.   Withdrawal of Certificates shall be communicated to other ExCBs and published in the IECEx Bulletin.

# Use of ExTRs and QARs for National Certification

## Documentation

For instances where separate national certification is required, the IECEx Scheme provides a fast track process through the acceptance of ExTRs and QARs.	ExCBs shall accept,  ExTRs and QARs issued by other ExCBs when issuing their own national certificates.   This does not preclude a technical review by the receiving ExCB in accordance with ISO/IEC Guide 65.  Any additional work  carried out by the ExCB receiving an ExTR and QAR shall not go beyond:

verify compliance with national differences from the IEC standards where those national differences have not been covered by the ExCB issuing the ExTR, and

adequately identify that the Ex equipment submitted for certification is that which is the subject of the ExTR and

verify compliance with national differences from IECEx reference document used for assessment of the quality system of the manufacturer where those national differences have not been covered by the ExCB issuing the QAR

## National Certification

When an applicant applies to an ExCB for its national certification or approval of Ex equipment on the basis of an ExTR, the application shall be accompanied by a copy of the ExTR.   In addition, the ExCB may request a sample of the Ex equipment and copies of the documentation referred to in the report for the purposes specified in10.1.

## Compliance with rules

The applicant shall follow the rules of procedure of the ExCB and shall confirm readiness to comply with all the relevant provisions regarding, for example, factory surveillance and payment of fees.

## Invalid ExTR

The ExCB may refuse to recognize the ExTR when the standard(s) or the amendments or editions of the standard(s) according to which it was issued is (are) no longer valid in the country of the ExCB. Such a change in validity shall have been notified in accordance with 7.4 and listed in the IECEx Bulletin as a national difference.

## Appeals

Should the ExCB receiving an ExTR or  QAR for recognition consider it to have been issued in error, the ExCB that issued the report shall be informed as soon as possible.   If the ExCBs involved arrive at different conclusions, the case may be referred to the Board of Appeal.

# Acceptance of certification bodies and assessment and testing laboratories

NOTE - When an application is made for acceptance of a certification body that intends to employ already accepted IECEx ExTLs, assessment is made according to this clause. Applications for acceptance of a certification body and an associated assessment and testing laboratory may be submitted together or as one combined application, and assessment according to 11.1 and 11.2 may be combined.

## Acceptance of certification bodies

### Conditions for acceptance

A certification body shall be accepted as an ExCB by the ExMC and given the right to issue IECEx Certificates of Conformity, ExTRs and QARs to specified standards, under the following conditions and according to the procedures stipulated in 11.1.2 to 11.1.14:

- the certification body shall be located in a participating country;

- the certification body shall operate a recognized certification or approval scheme at national level for the specified types of protection;

- the competence of the certification body to comply with these Rules shall be demonstrated by assessment.   The general competence, efficiency, experience, familiarity with the relevant standards and the types or concepts of protection included in those standards and competence to carry out quality management system assessments as well as compliance with ISO/IEC 65 shall be assessed.   Acceptance in another IEC Scheme or accreditation by a recognized national accreditation body shall be taken into account. In those cases, the ExMC shall decide upon the extent of the assessment that is necessary;

- the certification body shall have within its organization, or have an agreement to employ, an ExTL accepted by the ExMC according to these Rules for the relevant types of protection.

### Application

An application for the acceptance of a certification body for one or more standards accepted for use in the IECEx Scheme shall be made by the candidate certification body, via the national Member Body of the IECEx Scheme.

The application shall be submitted to the Secretary of the ExMC and shall be accompanied by a declaration as detailed in Annex B.

When, during the transitional period, certification or approval is needed in a country as a condition to supply a product for use in that country, the candidate certification body shall declare that the national certification or approval can be based on an ExTR.   When national differences or other conditions have to be fulfilled, they shall be as declared by the Member Body of the IECEx Scheme and published in the IECEx Bulletin.   There shall not be more than one set of national differences for each country.

The candidate certification body shall communicate the following information relevant to the recognition of ExTRs to the Secretary of the ExMC:

written information on procedures and rules for certification or approval at national level;

whether or not a foreign manufacturer is required to make application for certification or approval through a representative resident in that country.

### Assessment

The candidate certification body shall be assessed to determine that the conditions according to 11.1.1 are fulfilled.   The assessment shall be carried out by three assessors appointed by the ExMC.   The assessment team shall be led by a Lead Assessor appointed by the ExMC and shall include at least one member drawn from an ExCB.

When an assessment and testing laboratory is to be assessed on the same occasion, the assessment team shall include a member from an ExTL.

The candidate shall be given the names and current appointments of the assessors proposed to be appointed by the ExMC. Candidates may object "for cause" (reasons to be stated) to the appointment of the assessors.

The candidate to be assessed shall express its willingness to pay the professional fees of the assessors, the amount to be decided by the ExMC, and the reasonable travelling and living expenses arising from the assessment. An estimate of these expenses shall be provided to the candidate in advance and agreed by the candidate.

IECEx Assessment Teams shall report to the Secretary of the ExMC who shall manage all assessments to ensure assessments are carried out in a timely manner and in accordance with the requirements of the Scheme.

### Resolution of differences

During the assessment, the assessors shall prepare a draft report which shall be discussed with the management of the candidate certification body.   Efforts should be made to resolve any differences of opinion between the assessors and the candidate during this discussion.

### Report to ExMC

The assessors shall submit to the ExMC, with a copy to the representatives of the candidate certification body, a confidential report containing their findings and recommendations, taking into account the declaration submitted together with the application.   The candidate may attend an ExMC meeting or submit written comments in order to respond to enquiries regarding its application.

### Acceptance

The ExMC shall decide upon the acceptance of the candidate certification body at a meeting or by correspondence. In the latter case, the decision shall be reported to the next meeting of the ExMC and recorded in the minutes.

### Notification

If the decision of the ExMC is positive, the Secretary of the ExMC shall inform the candidate certification body in writing.

If the decision of the ExMC is negative, the Chairman of the ExMC may, depending on the findings, suggest to the candidate certification body

to withdraw the application, or

to accept a new assessment.

### Changes

Each ExCB shall inform the Secretary of the ExMC about changes in the information given according to 11.1.2 and 11.1.3.

### Extension of scope

When an ExCB wishes to extend its acceptance to further standards accepted for use in the IECEx Scheme, an application shall be made to the Secretary of the ExMC via the Member Body of the IECEx Scheme.   When the ExCB has been assessed within the last five years, the members of the Assessment Team which assessed the ExCB should give their comments on the application.

The ExMC shall decide whether the extension can be accepted on the basis of the information thus available, or whether a full or limited assessment will be needed.

The matter shall either be submitted to a meeting of the ExMC for decision or handled according to 11.1.11.

### Reporting of decisions

The ExMC may delegate the decisions according to 11.1.10 to the Chairman and Vice-Chairman of the ExMC to be made by correspondence between meetings. Such a decision shall be reported to the next meeting of the ExMC and recorded in the minutes.

### Re-assessment

By means of re-assessment to the extent and frequency deemed necessary, the ExMC shall verify whether ExCBs are still fulfilling the conditions of 11.1.1.

An ExCB wishing to withdraw from the IECEx Scheme shall notify the Secretary of the ExMC via the Member Body of the IECEx Scheme at least one year in advance and shall indicate the reason for the withdrawal and the date from which the withdrawal will become effective.

The acceptance of an ExCB may be suspended or withdrawn by the ExMC if that ExCB no longer fulfils the conditions of 11.1.1 or if in the opinion of the ExMC, the ExCB hampers the aim, operation or development of the IECEx Scheme, fails to take action regarding misuse of IECEx Certificates of Conformity or the IECEx Mark of Conformity*, or violates these Rules. Before such a decision is made, the ExCB shall be given the opportunity to take corrective action over a period of six months and state its own opinion on the matter.

A decision to suspend or withdraw the acceptance of an ExCB shall require agreement at a meeting of the ExMC by a majority of at least four fifths of the total number of members. Members not attending that meeting shall have the right to cast their vote in writing by registered mail to the Secretary of the ExMC prior to the meeting.

In case of a suspension or a withdrawal, the certification body in question shall not be allowed to claim any relationship with the IECEx Scheme.

## Acceptance of  Ex testing laboratories

NOTE - Applications for acceptance of a certification body and an associated assessment and testing laboratory may be submitted independently or as one combined application, in which case assessment according to 11.1 and 11.2 may be combined.

Acceptance of an  Ex testing laboratory as an ExTL is subject to the following conditions and to the procedures stipulated in 11.2.2 to 11.2.12:

- the  Ex testing laboratory shall be located in a participating country;

- an  Ex testing laboratory can operate as an ExTL if it is integral with an ExCB, under the complete technical and legal control of an ExCB or has a written agreement with an ExCB to undertake work with it according to these Rules;

- the competence of the assessment and testing laboratory shall be demonstrated by assessment. The general competence, efficiency, experience, familiarity with the relevant standards and the types of protection included in those standards as well as compliance with ISO/IEC 17025 and the IECEx Technical Guidance Documents shall be assessed. Acceptance in another IEC Scheme or accreditation by a recognized national accreditation body shall be taken into account.   The ExMC shall decide upon the extent of the assessment that is necessary.

An application for the acceptance of a laboratory as an ExTL for assessment and testing according to one or more standards accepted for use in the IECEx Scheme shall be made by the candidate assessment and testing laboratory, via the Member Body of the IECEx Scheme.

The application shall be submitted to the Secretary of the ExMC and shall be accompanied by a declaration as detailed in Annex C.

The candidate assessment and testing laboratory shall be assessed to determine that the conditions according to 11.2.1 are fulfilled. The assessment shall be carried out by three assessors appointed by the ExMC. The assessment team shall be led by a Lead Assessor appointed by the ExMC and shall include one member from an ExCB and one member from an ExTL.

When the laboratory is integral with a candidate certification body, or is to be assessed on the same occasion as a candidate certification body, a combined assessment team of three persons may be appointed.

The candidate shall be given the names and current appointments of the assessors proposed to be appointed by the ExMC.   Candidates may object "for cause" (reasons to be stated) to the appointment of the assessors.

The laboratory to be assessed shall express its willingness to pay the professional fees of the assessors, the amount to be decided by the ExMC, and the reasonable travelling and living expenses arising from the assessment.   An estimate of these expenses shall be provided to the candidate in advance and agreed by the candidate.

The Secretary of the ExMC shall manage the assessment process.

During the assessment, the assessors shall prepare a draft report which shall be discussed with the management of the candidate assessment and testing laboratory.   Efforts should be made to resolve any differences of opinion between the assessors and the candidate during this discussion.

The assessors shall submit to the ExMC, with a copy to the representatives of the candidate assessment and testing laboratory, a confidential report containing their findings and recommendations, taking into account the declaration submitted together with the application. The candidate may attend an ExMC meeting or submit written comments to respond to enquiries regarding its application.

The ExMC shall decide upon the acceptance of the candidate Ex testing laboratory at a meeting or by correspondence. In the latter case, the decision shall be reported to the next meeting of the ExMC and recorded in the minutes.

If the decision of the ExMC is positive, the Secretary of the ExMC shall inform the candidate assessment and testing laboratory in writing.

If the decision of the ExMC is negative, the Chairman of the ExMC may, depending on the findings, suggest to the candidate assessment and testing laboratory

- to withdraw the application, or

- to accept a new assessment.

When an ExTL wishes to extend its acceptance to further standards accepted for use in the IECEx Scheme, an application shall be made to the Secretary of the ExMC via the Member Body of the IECEx Scheme. When the ExTL has been assessed within the last five years, the members of the Assessment Team which assessed the ExTL should give their comments on the application.

The ExMC shall decide whether the extension can be given on the basis of the information thus available, or whether a full or limited assessment will be needed.

The matter shall be submitted to the ExMC for decision at a meeting or handled according to 11.2.10.

The ExMC may delegate the decisions according to 11.2.9 to the Chairman and Vice-Chairman of the ExMC to be made by correspondence between meetings.   Such a decision shall be reported to the next meeting of the ExMC and recorded in the minutes.

By means of re-assessment and comparative assessment and testing to the extent and frequency deemed necessary, the ExMC shall verify whether the ExTLs are still fulfilling the conditions of 11.2.1.

The acceptance of an ExTL may be suspended or withdrawn by the ExMC if that ExTL no longer fulfils the conditions of 11.2.1 or if it violates these Rules.   Before such a recommendation is made, the ExTL shall have the opportunity to take corrective action over a period of six months and state its own opinion on the matter.

In case of a suspension or a withdrawal, the assessment and testing laboratory in question shall not be allowed to claim any relationship with the IECEx Scheme.

### ExTR Review

As a means of ensuring confidence, among Scheme Members, newly accepted ExTLs shall submit a copy of the first completed ExTR to the ExMC Secretary who will arrange for it to be reviewed.  The outcome of this review may require corrective actions to be undertaken by the ExTL and review of further ExTRs.

# IECEx publications

## Types of publications

Three publications shall be produced:

the IECEx Register;

the IECEx Bulletin;

the IECEx Newsletter.

NOTE - The ExMC may decide to issue the publications in electronic format and may be contained within an IECEx Internet Website.  The Register and  Bulletin may be produced as one publication.

## Information to be available

The following information shall be made readily available, to the public.

ExCBs and ExTLs,

manufacturers holding IECEx Certificates of Conformity,

IECEx Certificates of Conformity issued,

categories of Ex equipment covered by the IECEx Scheme, and

standards accepted for use in the IECEx Scheme.

## IECEx Bulletin

The IECEx Bulletin shall be issued at intervals decided by the ExMC. It shall contain information on

the standards for which ExCBs in each country have declared recognition of ExTRs,

national differences for each standard and country as declared by the Member Bodies of the IECEx Scheme,

important rules in addition to the content of the standards which have to be fulfilled in the countries during the transitional period,

the standards for which ExCBs in each country are authorized to issue IECEx Certificates of Conformity,

the operation of the IECEx Scheme, to assist the applicants, and IECEx Certificates of Conformity withdrawn.

## IECEx Newsletter

The IECEx Newsletter shall be used to publicise developments within the IECEx Scheme, including new ExCBs and ExTLs joining the IECEx Scheme, matters relating to relevant IEC standards and changes in the Rules.

## Source of information

The information published in the IECEx publications is based on information given by the Member Bodies of the IECEx Scheme, ExCBs and ExTLs. Neither the IEC nor the Secretary of the ExMC is therefore liable for the accuracy of that information. Publication of commercial information shall be avoided.

# Complaints

If there are complaints concerning the actions of an ExCB or an ExTL that the ExMC cannot resolve, the ExMC or the complainant shall have the right to request the CAB to take appropriate action.

Application from a candidate Member Body of the IECEx Scheme
 to become a participating country in the IECEx Scheme

(normative)

The application from a candidate Member Body of the IECEx for its country to become a participating country in the IECEx Scheme shall be a self-contained document including the following information:

- the name of the country;

- the name and address of the candidate Member Body of the IECEx Scheme;

- the legal status of the candidate Member Body of the IECEx Scheme;

- the IEC standard(s) for which participation is sought;

- the national standard(s) corresponding to the IEC standard(s) listed in d);

- any national differences from the IEC standard(s);

- whether or not IECEx Certificates of Conformity are accepted in the country;

- where national differences exist or where IECEx Certificates of Conformity are not accepted in the country, a proposed transitional period during which national standards and IEC standards would become identical and acceptance of IECEx Certificates of Conformity would be achieved;

- an undertaking that the applicant will abide by the Rules and use its best endeavours to assist in the achievement of the aims and objectives of the IECEx Scheme.

Declaration by a certification body applying
to become an Ex Certification Body

(normative)

The declaration by a certification body applying to become an Ex Certification Body (ExCB) shall be a self-contained document including the following information:

- a description of the body which gives, in addition to an organization chart, information about

the legal status of the body,

the address(es) at which it carries out its operations,

the means by which the body will demonstrate compliance with ISO/IEC Guides 62 and 65,

the legal relationship between the body and the assessment and testing laboratory(ies) used in the course of its work (including the case where the assessment and testing laboratory is integral with the certification body),

the responsibilities at national level concerning certification, and the schemes operated,

the arrangements for appeal,

the arrangements for recognition of IECEx Certificates of Conformity, IECEx Ex Test Reports (ExTRs) and IECEx Quality Assessment Reports (QARs) when issuing its own national or regional certificates.

the documents available for providing supporting information, for example with regard to existing accreditation;

Details of Senior Management with competence in the certification of Ex equipment

a list of the standards accepted for use in the IECEx Scheme according to which the body wishes to issue IECEx Certificates of Conformity;

a statement that the body will recognize ExTRs and QARs produced by other ExCBs when issuing its national or regional certificates or approvals, during the transitional period;

a list of the standards accepted for use in the IECEx Scheme, including details of the edition and amendments if any, which are accepted in whole or in part by the body when issuing its national or regional certificates or approvals. Where national differences from the standards exist, these shall be declared for later publication in the IECEx Bulletin;

a statement of the number of certificates issued in the preceding two years for each type of protection covered by the standards listed in b) and d);

a statement that the body will abide by the Rules.

Declaration by an assessment and testing laboratory applying
for acceptance as an IECEx  Ex Testing Laboratory

(normative)

The declaration by an assessment and testing laboratory applying for acceptance as an IECEx Assessment and Testing Laboratory shall be a self-contained document including the following information:

- a description of the laboratory, which gives, in addition to an organization chart, information about

relationship between the laboratory and the relevant Ex Certification Body or Accepted Certification Bodies,

the legal status of the laboratory,

the address(es) at which it carries out its operations,

the responsibilities concerning assessment and testing,

the means by which the laboratory will demonstrate compliance with ISO/IEC 17025, and

the documents available for providing supporting information, for example with regard to existing accreditation;

a list of the standards accepted for use in the IECEx Scheme according to which the laboratory intends to conduct tests;

the information required in annex D;

a statement of the number of test reports issued in the preceding two years for each type of protection covered by the standards listed in b);

a statement that the laboratory will abide by the Rules.

Information to be provided by an assessment
and testing laboratory in applying for acceptance

(normative)

NOTES

1.    The text of this annex is taken from the annex to ISO/IEC Guide 38 1983 which is now obsolete.

2.    Throughout the text, the word "recognition" should be taken to mean "acceptance" in the context of the IECEx Scheme.

Applicant's name and address:

Telephone No:

Telefax No:

Test Laboratory* name and address (if different from paragraph 1):

Telephone No:

Telefax No:

Senior management

Names and titles of the senior executives of the Test Laboratory* and of the assessment and testing laboratories for which recognition is being sought:

Name and title of the person responsible for the Quality Management System in the assessment and testing laboratory:

Name and title of the principal contact nominated by the assessment and testing laboratory, and of his deputy:

Operating departments of the assessment and testing laboratory for which recognition is being sought. (Show on a separate sheet to be attached either as a list or as an organization chart of the Test Laboratory*.):

Employees

Total number in Test Laboratory*:

Total number in assessment and testing laboratory for which recognition is being sought:

Total number of professionally qualified staff (see also ISO/IEC 17025) in the area for which recognition is being sought:

Equipment

List on a separate sheet the major items of test equipment available for use in the area for which recognition is being sought.

Test facilities and services

List on a separate sheet the assessment and testing services for which recognition is being sought, indicating for each service any limits between which it will operate, and the published specifications against which the assessment and testing will be performed.

If recognition by other bodies or authorities is held in the area for which recognition is being sought, please give details.

What type of assessment and testing  is to be subcontracted in respect of the recognition being sought?

*  "Test Laboratory" refers here to the corporate entity having final authority over the "assessment and testing laboratory" seeking recognition. In some cases this may be the same body.

Other information

Document, where applicable, how the assessment and testing laboratory may be related to external organizations or to components within its own parent organization.

Give any other information which you consider could be of assistance to the assessment team (on a separate sheet if necessary).

Yes/No	Particulars
	(where appropriate)

Quality Management Policy

Are policy and procedures for the operation of the assessment and testing laboratory contained in a document such as a Quality Manual?

Has the person responsible for quality management the responsibility and authority to identify quality problems and initiate effective solutions?

Does the Quality Manual contain procedures for the supervision of any unqualified staff (see also ISO/IEC 17025)?

Is there a prescribed audit procedure for checking quality management functions?

Work instructions

Are manuals, work instructions and regulations to be used by staff readily available?

Is there a system for updating, implementing and recording changes to these documents?

Are documents available for each assessment and testing operation?

Are documents and reference data maintained in an up-to-date condition?

Is obsolete data promptly removed from documents, etc.?

Personnel

Have standards of professional ability, skills and job descriptions been prescribed where necessary?

Are training methods applied to attain and maintain skills with due attention to quality requirements?

Test equipment and calibration

Does the Quality Management System specify that the equipment is of accuracy compatible with the assessment and testing undertaken?

Is a record maintained of all test equipment, including calibration results?

Are facilities and appropriate environments provided for calibration, handling, control, storage and maintenance of all assessment and testing and measuring equipment?

Are there documented procedures for calibrating all equipment and reference standards, which include method, periodicity, sealing after calibration, etc.?

If not, explain calibration system used:

Are reference standards used for calibration traceable to national or international standards of measurement?

Test procedures

Are test methods and procedures recorded which are not called up in specifications, manuals, etc.?

Yes/No	Particulars
	(where appropriate)

Are the environments in which tests are conducted and results recorded suitable to ensure their accuracy?

Do environmental test facilities exist?

Is there control of access to the assessment and testing areas?

Is there a prescribed system for detecting deficiencies in assessment and testing and their causes, and for correcting unfavourable trends?

Handling and storage

Are work and inspection instructions prescribed and implemented for the handling, storage and return to the client of materials and samples?

Are appropriate storage areas arranged to prevent deterioration or damage to the products concerned?

Are storage methods prescribed, including special environments?

Are there procedures for the inspection of samples in storage?

Are storage areas accessible only to authorized persons?

Is provision made to ensure that all samples to be stored or returned to the client are adequately identified and labelled?

Records

Is there a prescribed system for recording the method and results of assessment and testing activities?

Are observations and calculations recorded and stored as to provide a permanent test record?

Are there arrangements for ensuring that records are current, complete, accurate and held confidential where required?

Test reports

Do test reports contain all the information required for such by ISO/IEC 17025?

Is the assessment and testing laboratory prepared to make arrangements to send copies of test reports to the body granting recognition, where required, on a strictly confidential basis?

Preparedness for assessment

Are you satisfied that you can meet all the requirements prescribed herein?

At what date will the assessment and testing laboratory be ready for assessment?

Is there any special urgency for assessment?

If so, what is the reason?

Applicant's name:

Signature of person authorized to sign for the Applicant:

(Title)

Date:	...............................................

Application for assessment as a recognized assessment and testing laboratory

| Name of applicant: | Name and address of assessment and testing laboratory if different: |
| --- | --- |
| Address: |  |
| Name of contact: | Name of contact: |
| Title: | Title: |
| Test or series of tests for which recognition is sought: |
| The assessment and testing laboratory hereby agrees to undertake: a) to conform to the requirements for a recognized assessment and testing laboratory; b) to pay all costs connected with assessment and administration in the pre-recognition stage irrespective of whether or not recognition is granted. |
| Signed: |
| (Title) |
| Date: |

End of Draft

# Text boxes

Manufacturer
submits
application
to ExCB 1

ExCB 1 arranges
for associated
ExTL to
conduct Testing

ExTL issues completed ExTR
 to ExCB 1

ExCB 1 or Manufacturer arranges for other ExCB to conduct audit

ExCB 1
conducts audit of Manufacturer’s quality system

ExCB 1 
prepares QAR

Alternate ExCB prepares QAR

ExCB 1 reviews and endorses ExTR

ExCB 1 reviews and endorses QAR

ExCB 1 issues:
IECEx CoC
IECEx ExTR
IECEx QAR
to applicant
(copy of CoC plus ExTR & QAR details to ExMC secretary

ExCB 1 instigates surveillance arrangements

No

Yes