This document prepared by TestSafe, AU, from PTB’s - short study - ExTAG/517C/DA presented at ExTAG(Cannes/PTB)03  2018  is issued for discussion under Agenda item 5.1 Intrinsic Safety – Spark Assessment for the combination of resistive, 	capacitive and inductive Parameters.

Below table is extracted from PTB short study ExTAG/517C/DA presented at ExTAG(Cannes/PTB) 2018

| Test series 900 nF |  |
| --- | --- |
| U / V | 20 | 20 | 17.2 (14% reduction in voltage) | Allowable value from Table A.1 & A.2 @ 17.2 V | Reduction of capacitance & current required from the standard to obtain probability of w ≈ 10¯³ (Pass) (%) |
| C / nF | 900 | 900 | 900 | 1660 | 54% (900/1660) |
| R / Ω | 10k | 43 Ω (464 mA) | 43 Ω (400 mA) | 770 mA | 51.9% (400/770) |
| τ / ms | 9 | 0.039 | 0.039 |  |  |
| x / contacts | 370 | 16 | 1274 |  |  |
| w | 2.7 x 10¯³ | 61 x 10¯³ (High Risk Ignition) | 0.79 x 10¯³ |  |  |

Table 3

TestSafe Comments:

As recommended by PTB, the voltage need to be reduce by 15% to get the probability of w ≈ 10¯³, by reducing the voltage, the allowable current and capacitance from Table A.1 & A.2 are much bigger. As shown above the reduce percentage for both current and capacitance are around 50% to get the probability of w ≈ 10¯³ (Pass).

Conclusion:

- The Safety Factor requirement of the standard is highly affected if full value of current and capacitance from Table A.1 & A.2 are used in combination.

- The reduction in voltage in PTB short study paper has a significant impact to the current and capacitance value.

- The new curves in figure 2 below recommended by PTB is an approximate 50% reduction of current and capacitance from IEC 60079-11 Figure A.1 & Figure A.3 curves. It is not to the lowest decoupling resistances. Would suggest reducing the capacitance value until the probability of 
w ≈ 10¯³ is reached, instead of reducing the voltage. This method would verify if the safety factor is affected when the maximum current from curve/table is used.

Above figure is extracted from PTB revised short study v2-1.